## Slide 1: The Challenge of Time-Predictability in Modern Many-Core Architectures
Vincent Nelis
WCET workshop 2014

## Slide 2: What’s a many-core platform?

## Slide 3
“Many-core processors are defined as chips with several tens, but more likely hundreds, or even thousands of processor cores”
-- András Vajda
András Vajda. Programming Many-Core Chips.
ISBN: 978-1-4419-9738-8 (Print) 978-1-4419-9739-5 (Online)
A many-core platform is a platform containing many cores.
Notes: Many-core is too many cores

## Slide 4
A many-core platform, it is like an entire distributed system squeezed into a single chip.
“A distributed system is a software system in which components located on networked computers communicate and coordinate their actions by passing messages.”
-- Coulouris, George; Jean Dollimore; Tim Kindberg; Gordon Blair (2011). Distributed Systems: Concepts and Design (5th Edition). Boston: Addison-Wesley.

## Slide 5
A many-core platform, it is like an entire distributed system squeezed into a single chip.
Mix between parallel computing where all processors communicate through a shared memory, and distributed computing, where memory is distributed and processors communicate by passing messages.

## Slide 6
Local Mem[s]
Network Interface
Processing unit[s]
Local Mem[s]
Network Interface
Processing unit[s]
Local Mem[s]
Network Interface
Processing unit[s]
Local Mem[s]
Network Interface
Processing unit[s]
External Mem[s]
NoC
Quick overview of the architecture
Notes: It can be hierarchical

## Slide 7
What types of application it is designed for?
Provide huge computing power through parallelization → HPC
May provide low-power and isolation? → Embedded
HPC
Best effort
“The faster, the better”
EC
Strong guarantees
“The safer, the better”
Embedded CEP, B-critical, etc.
Notes: Event processing is a method of tracking and analyzing (processing) streams of information (data) about things that happen (events),[1] and deriving a conclusion from them. Complex event processing, or CEP, is event processing that combines data from multiple sources[2] to infer events or patterns that suggest more complicated circumstances. The goal of complex event processing is to identify meaningful events (such as opportunities or threats)[3] and respond to them as quickly as possible.
These events may be happening across the various layers of an organization as sales leads, orders or customer service calls. Or, they may be news items,[4] text messages, social media posts, stock market feeds, traffic reports, weather reports, or other kinds of data.[1]An event may also be defined as a "change of state," when a measurement exceeds a predefined threshold of time, temperature, or other value. Analysts suggest that CEP will give organizations a new way to analyze patterns in real-time, and help the business side communicate better with IT and service departments.[5]

## Slide 8
Embedded Complex Event Processing
Notes: A more systemic example of CEP involves a car, some sensors and various events and reactions. Imagine that a car has several sensors—one that measures tire pressure, one that measures speed, and one that detects if someone sits on a seat or leaves a seat.
In the first situation, the car is moving and the pressure of one of the tires moves from 45 psi (pound per square inch) to 41 psi over 15 minutes. As the pressure in the tire is decreasing, a series of events containing the tire pressure is generated. In addition, a series of events containing the speed of the car is generated. The car's Event Processor may detect a situation whereby a loss of tire pressure over a relatively long period of time results in the creation of the "lossOfTirePressure" event. This new event may trigger a reaction process to note the pressure loss into the car's maintenance log, and alert the driver via the car's portal that the tire pressure has reduced.
In the second situation, the car is moving and the pressure of one of the tires drops from 45 psi to 20 psi in 5 seconds. A different situation is detected—perhaps because the loss of pressure occurred over a shorter period of time, or perhaps because the difference in values between each event were larger than a predefined limit. The different situation results in a new event "blowOutTire" being generated. This new event triggers a different reaction process to immediately alert the driver and to initiate onboard computer routines to assist the driver in bringing the car to a stop without losing control through skidding.
In addition, events that represent detected situations can also be combined with other events in order to detect more complex situations. For example, in the final situation the car was moving normally but suffers a blown tire which results in the car leaving the road and striking a tree and the driver is thrown from the car. A series of different situations are rapidly detected. The combination of "blowOutTire", "zeroSpeed" and "driverLeftSeat" within a very short space of time results in a new situation being detected: "occupantThrownAccident". Even though there is no direct measurement that can determine conclusively that the driver was thrown, or that there was an accident, the combination of events allows the situation to be detected and a new event to be created to signify the detected situation. This is the essence of a complex (or composite) event. It is complex because one cannot directly detect the situation; one has to infer or deduce that the situation has occurred from a combination of other events.

## Slide 9
Parallel Software Framework for Time-Critical Many-core Systems
Goal: allow current and future applications with high-performance and real-time requirements to fully exploit the huge performance opportunities brought by the most advanced many-core processors, whilst ensuring a predictable performance and maintaining (or even reducing) development costs of applications.
Purpose: develop a new design framework, from the conceptual design of the system functionality to its physical implementation, to facilitate the deployment of standardized parallel architectures in all kinds of systems.
Notes: P-SOCRATES (Parallel Software Framework for Time-Critical Many-core Systems) is an European project which intends to allow current and future applications with high-performance and real-time requirements to fully exploit the huge performance opportunities brought by the most advanced many-core processors, whilst ensuring a predictable performance and maintaining (or even reducing) development costs of applications.
The purpose of P-SOCRATES is to develop an entirely new design framework, from the conceptual design of the system functionality to its physical implementation, to facilitate the deployment of standardized parallel architectures in all kinds of systems.

## Slide 11
Regarding the time-predictability, we have identified a few main challenges that we will need to take up before the end of the project.
And that’s why I’m here today...
Interested?
-> nelis@isep.ipp.pt
00 351 91 206 68 04

## Slide 12
Challenge number 1
Define a suitable application model

## Slide 13
Liu & Layland and all derivatives
Ci , Ti
Oi = Oj
Oi ≠ Oj
Ci < Dj
Ci = Dj
Ci > Dj
Ti = kTj
Ti ≠ Tj
Ti = Tj
Ci = [ck,..., cl]
Ti spor.

## Slide 14
Liu & Layland and all derivatives
Ci , Ti
Oi = Oj
Oi ≠ Oj
Ci < Dj
Ci = Dj
Ci > Dj
Ti = kTj
Ti ≠ Tj
Ti = Tj
Ci = [ck,..., cl]
Ti spor.
Model the timing aspects only
No information on
  The inner structure of the task
  The functional properties
  The parallelization opportunities
  Etc.
Not rich enough!

## Slide 15
And what about the // task models?
Data
Task

## Slide 16
Data parallelism
Core “A”
Core “B”
if Core = A
lower_limit := 1
upper_limit := 4
else if Core = B
lower_limit := 5
upper_limit := 8
for i from lower_limit to upper_limit by 1
foo(Array[i])
Array =
foo([5, 18])
foo([9, 3])
5 | 18 | 9 | 3

## Slide 17
Data parallelism
Array =
5 | 18 | 9 | 3
foo([5, 18])
foo([9, 3])
fork
join
WCET
Precedence
constraint
Fork/join task model

## Slide 18
Task parallelism
if Core = A
for i from 1 to 4 by 1
func(Array[i])
else if Core = B
for i from 1 to 4 by 1
otherfunc(Array[i])
Array =
func([5, 18, 9, 3])
otherfunc([5, 18, 9, 3])
5 | 18 | 9 | 3
Core “A”
Core “B”

## Slide 19
Task parallelism
Array =
func([5, 18, 9, 3])
otherfunc([5, 18, 9, 3])
5 | 18 | 9 | 3
for i from 1 to 4 by 1
func(Array[i])
for i from 1 to 4 by 1
otherfunc(Array[i])
Actor “X”
Actor “Y”
Core “A”
Core “B”
if Core = A
for i from 1 to 4 by 1
func(Array[i])
else if Core = B
for i from 1 to 4 by 1
otherfunc(Array[i])

## Slide 20
Task parallelism
Array =
5 | 18 | 9 | 3
Core “A”
Core “B”
Actor “X”
WCET
Actor “Y”
WCET
data
dependency
Precedence
constraint
func([5, 18, 9, 3])
for i from 1 to 4 by 1
func(Array[i])
Actor “X”
otherfunc([5, 18, 9, 3])
for i from 1 to 4 by 1
otherfunc(Array[i])
Actor “Y”

## Slide 21
Task parallelism
Actor “A”
WCET
Actor “C”
WCET
Actor “D”
WCET
Actor “G”
WCET
Actor “B”
WCET
Actor “E”
WCET
Actor “H”
WCET
Actor “J”
WCET
Actor “K”
WCET
Actor “I”
WCET
Actor “F”
WCET
DAG task model

## Slide 22
x := A()
if (x > 1) {
#pragma omp parallel for reduction(+:y)
for (i=0; i<4; i++)
y := B(i)
} else {
#pragma omp parallel for reduction(+:y)
for (i=0; i<2; i++)
y := C(i)
}
z := D(y)
A()
D(y)
B(0)
B(1)
B(2)
B(3)
C(0)
C(1)
Execution path
What are the limitations of these models?

## Slide 23
None of these models properly capture the conditional execution!
Let’s have a look at how the F/J and DAG model this task...
x := A()
if (x > 1) {
#pragma omp parallel for reduction(+:y)
for (i=0; i<4; i++)
y := B(i)
} else {
#pragma omp parallel for reduction(+:y)
for (i=0; i<2; i++)
y := C(i)
}
z := D(y)

## Slide 24
WCET
WCET
WCET
WCET
WCET
WCET
WCET
WCET
Option 1:
Ignore the conditional execution
A()
D(y)
B(0)
B(1)
B(2)
B(3)
C(0)
C(1)

## Slide 25
WCET
WCET
WCET
WCET
WCET
WCET
WCET
WCET
It assumes that every single line of the code of the task is executed each time the task is run, including the code of every if and else statement, every function, etc.
Option 1:
Ignore the conditional execution

## Slide 26
Option 2:
Identify the worst-case execution path
Challenge
number 2

## Slide 27
Challenge number 2
Identify the worst-case execution path in a parallel program
Not this way
Not this way
Not this way

## Slide 28
What does it mean:
“worst-case” execution path?
From a response time point of view, the “worst-case” execution path is the one that creates the maximum interference on the other tasks
Sequential task
worst-case execution path = longest path
Notes: What do we mean by
“worst-case execution path”?

## Slide 29
x := A()
if (x > 1) {
#pragma omp parallel for reduction(+:y)
for (i=0; i<4; i++)
y := B(i)
} else {
#pragma omp parallel for reduction(+:y)
for (i=0; i<2; i++)
y := C(i)
}
z := D(y)
A()
D(y)
B(0)
B(1)
B(2)
B(3)
C(0)
C(1)
Execution path

## Slide 30
A()
B(0)
D(y)
B(1)
B(2)
B(3)
C(0)
C(1)
A()
D(y)
“if” path
“else” path
Workload (W) = 43
Crit. Path (CP) = 23
Conc. Level (CL) = 2
Workload (W) = 45
Crit. Path (CP) = 22
Conc. Level (CL) = 4
1
4
8
11
19
2
A()
B(0)
D(y)
B(1)
B(2)
B(3)
20
20
C(0)
C(1)
1
A()
2
D(y)
Notes: What do we mean by
“worst-case execution path”?

## Slide 31
1
4
8
11
19
2
A()
B(0)
D(y)
B(1)
B(2)
B(3)
20
20
C(0)
C(1)
1
A()
2
D(y)
Workload (W) = 43
Crit. Path (CP) = 23
Conc. Level (CL) = 2
Workload (W) = 45
Crit. Path (CP) = 22
Conc. Level (CL) = 4
HP
LP
10
Response time
“if” path
“else” path
Notes: What do we mean by
“worst-case execution path”?

## Slide 32
Case 2: the “else” path
4
time
1
8
11
19
2
1
9
Case 1: the “if” path
Response time = 22
20
time
1
20
2
1
9
Response
time = 30

## Slide 33
time
11
19
9
Response time = 14
time
Response time = 10
4
1
8
2
1
20
1
20
2
1
9

## Slide 34
Task 2: LOW
Max Conc. Lvl
Task 1: HIGH
Max Workload
Max Crit. Path
Max Conc. Lvl
Max Workload
Max Crit. Path
Lead to worst-case
response time

## Slide 35
Sequential task
worst-case execution path = longest path
Identify the worst-case execution path in a parallel program (from a schedulability point of view)
Challenge number 2
Parallel task
worst-case execution path = ???
Notes: What do we mean by
“worst-case execution path”?

## Slide 36
Challenge number 3
Even if we know what’s the worst path, how do we find it?

## Slide 37
The number of execution paths is extredibly high
for(int i=0; i<N; i++) {
if(i > x) cilk_spawn func(i);
}
Intuitively, we want to think that x > N is the worst-case scenario, but is it?

## Slide 38
The number of execution paths is extredibly high
Void compute (int* A, int i, int j) {
#pragma omp task depend(out:A[i])
Produce(&A[i])
#pragma omp task depend(in:A[j])
Consume(&A[j])
}
Depending if i=j or i<>j, at runtime we will have
P
C
P
C
i=j
i<>j

## Slide 39
Even if we know what’s the worst path, how do we find it?
entry
exit

## Slide 40
Challenge number 4
What about the use and impact of the shared resources?

## Slide 41
WCET
WCET
Cache
WCET
WCET
WCET
WCET
What matters is “when” the task executes, not “where”.
Memory

## Slide 42
Memory
What matters is “when” the task executes, not “where”.
Now, the position matters.

## Slide 43
Challenge number 5
What about the implementation?

## Slide 44
Local Mem[s]
Network Interface
Processing unit[s]
Local Mem[s]
Network Interface
Processing unit[s]
Local Mem[s]
Network Interface
Processing unit[s]
Local Mem[s]
Network Interface
Processing unit[s]
External Mem[s]
NoC
Quick overview of the architecture

## Slide 45
Local Mem[s]
Network Interface
Processing unit[s]
Local Mem[s]
Network Interface
Processing unit[s]
Local Mem[s]
Network Interface
Processing unit[s]
Local Mem[s]
Network Interface
Processing unit[s]
External Mem[s]
NoC
A()
D(y)
B(0)
B(1)
B(2)
B(3)
C(0)
C(1)

## Slide 46
Summary
Plenty of new problems for everybody and no “smart” solutions so far
  At the modelling level
  At the WCET and scheduling analysis level
  At the implementation level
  If you find a solution to one of these problems or you wish to collaborate with us on solving them:
  nelis@isep.ipp.pt
  +351 91 206 68 04

## Slide 47
Thank you
for inviting me,
for listening to me,
and for helping us solve these problems

## Slide 48
Expert System

## Slide 49
user
News
provider

## Slide 50
user
News
provider
Companies
How do I pick the right ads?

## Slide 51
Expert
System
user
News
provider
Companies

## Slide 52
Expert
System
user
News
provider
Companies

## Slide 53
Expert
System
News
provider
user
Companies
  Condition 1:
  Do your job properly!

## Slide 54
  What does that mean?

## Slide 55
  My jaguar
  consumes a lot
  of meat.
  gaz

## Slide 56
Expert
System
user
News
provider
Companies
  Condition 1:
  Do your job properly!
  Condition 2:
  Do it on time!
10
milli-seconds!
Notes: Check the 4

## Slide 57: Solution?
Task:
To be used in the sched. analysis
Creates the max interference